## Slide 1
PBL • REVIEW 4 • FULL STACK WEB DEVELOPMENT
DIGITAL TWIN FACTORY
Real-Time Industrial Monitoring and Predictive Maintenance System
A connected view of machines, sensor telemetry, alarms and maintenance
Y. Swajith • C. Vanshika • Y. Somanath • Prabhu Charan Course: Full Stack Web Development (25SC2008E) | Guide: Dr. Chiranjeevi
Koneru Lakshmaiah Education Foundation

## Slide 2
The problem we are addressing
Why a digital-twin monitoring view is useful
SCATTERED SIGNALS
Sensor values and machine status can be difficult to review when separated across devices.
LATE VISIBILITY
Abnormal temperature, vibration or pressure needs attention before it becomes a larger operational issue.
FOLLOW-UP GAP
Teams need a shared way to review alarms and track maintenance work.
Project goal: bring telemetry, machine status, alarm history, trends and maintenance actions into one dashboard.
This is a monitoring and decision-support prototype—not a certified machine-control or safety system.

## Slide 3
System architecture
The full data path from sensor source to dashboard
EDGE / SIMULATOR
ESP32 / Wokwi Virtual machines
→
MQTT BROKER
Publish / subscribe JSON telemetry
→
PYTHON INGESTION
Validate • store Alarm rules
→
POSTGRESQL
Readings • alarms Thresholds • work orders
→
FASTAPI + SSE
REST endpoints Live snapshots
→
REACT DASHBOARD
3D twin • charts Alerts • maintenance
Live updates use Server-Sent Events (SSE). MQTT carries telemetry; PostgreSQL persists it.

## Slide 4
Technology stack
Each layer has a clear responsibility
DEVICE / DATA
ESP32/Wokwi + Python simulator
MESSAGING / STORAGE
MQTT + PostgreSQL
BACKEND
Python ingestion + FastAPI
FRONTEND
React + Vite
VISUALIZATION
Three.js / React Three Fiber + charts
Separation of concerns makes it easier to debug, extend and test each layer.

## Slide 5
What the operator sees
One interface for fleet health and investigation
OVERVIEW
Fleet status, online machines, active alarms and system indicators.
MACHINE DETAIL
Sensor readings and machine-specific threshold context.
HISTORY & ANALYTICS
Time-series views and trend/anomaly indicators.
3D FACTORY
Digital representation of assets and status.
ALERTS & MAINTENANCE
Acknowledge alarms and track work orders.

## Slide 6
Alarm and maintenance workflow
From a sensor signal to an action
1
Sensor reading arrives
2
Ingestion validates payload
3
Threshold logic checks conditions
4
Alarm is stored and shown
5
Operator acknowledges / investigates
6
Maintenance work order is tracked

## Slide 7
Analytics: useful, but honest
What the indicators mean—and what they do not
HEALTH INDEX
A computed indicator based on distance to configured limits, trends and anomalies.
TREND HINTS
Statistical trend and z-score logic can flag readings approaching a threshold.
NOT A GUARANTEE
These are heuristics, not a trained or safety-certified failure predictor.
OEE is not implemented from real production data: verified PLC production counters and cycle-time inputs are required.
“Availability (24 h)” in the dashboard means data availability—not production uptime.

## Slide 8
Live demo sequence
A short, reliable walkthrough for faculty
• Open Overview and confirm that the API, database and telemetry pipeline are healthy.
• Show sensor values and machine connectivity on the Machines page.
• Trigger or wait for a simulator alarm; open Alerts and acknowledge it.
• Open Analytics/History to explain a trend and the evidence behind it.
• Create or update a maintenance work order if the live setup supports it.
• Finish on the 3D factory view and explain the operational benefit.

## Slide 9
Deployment and reliability
What must be running for a successful demonstration
DATABASE
PostgreSQL reachable; correct DATABASE_URL or DB_* values; schema initialized.
BACKEND
FastAPI and MQTT subscriber running once each; correct database and broker settings.
FRONTEND + SOURCE
Vercel origin allowed by CORS; API URL points to the deployed API; simulator/device publishes.
If /api/health/db fails, resolve database URL, credentials, network access and schema before the demo.
Never commit passwords, private .env files or exposed secrets to GitHub.

## Slide 10
Practical value and social/industry impact
What the project can help a team do
VISIBILITY
Inspect machine readings and connectivity in one place.
EARLIER INVESTIGATION
Notice abnormal signals and investigate before the issue grows.
ACCOUNTABILITY
Keep alarm history and track maintenance tasks.
Potential benefit: more organized monitoring and maintenance decisions. Real-world benefit must be validated with real assets and data.

## Slide 11
Limitations and future work
Path from prototype to industrial deployment
REAL PLC DATA
Add verified production counts, cycle times and calibrated sensor feeds.
SECURITY
Server-side authentication, roles, TLS, secrets management and broker ACLs.
VALIDATION
Test alarms, predictions, backups and container deployment against acceptance criteria.
• Validate prediction methods against representative failure data.
• Integrate OEE only when reliable production counters are available.

## Slide 12
CONCLUSION
Digital Twin Factory connects IoT telemetry to an actionable, visual operations dashboard.
It demonstrates full-stack integration across messaging, storage, APIs, live updates, analytics and maintenance workflows.
Thank you
GitHub: https://github.com/swajith-26/Digital-twin-Factory Guide: Dr. Chiranjeevi